Applications of Area (MTMH89) The learner will solve problems relating to area. Author - Wade Wells

Question 1: A rectangular strip is 9.00 inches long and 7.00 inches wide. Find the area of the strip in square feet. Round to the nearest hundredth. Answer 1: 63.00 sq ft Answer 2: 0.44 sq ft Answer 3: 5.25 sq ft Answer 4: 0.62 sq ft Correct Answer: 0.44 sq ft

Question 2: A sheet metal square contains 841 square inches. Find the length, to the nearest inch, of each side of the square sheet. Answer 1: 17 in Answer 2: 210 in Answer 3: 39 in Answer 4: 29 in Correct Answer: 29 in

Question 3: The cost of a rectangular plate of aluminum that is 2 feet wide and 3 feet long is $22.50. Using the same stock, find the cost of a rectangular plate that is 5 feet wide and 8 feet long. Answer 1: $75.75 Answer 2: $150.00 Answer 3: $58.50 Answer 4: $185.25 Correct Answer: $150.00

Question 4: The support base shown has an area of 3685 square millimeters. Calculate unknown dimension x to the nearest tenth of a millimeter. Answer 1: 40.8 mm Answer 2: 36.3 mm Answer 3: 42.5 mm Answer 4: 38.0 mm Correct Answer: 38.0 mm

Question 5: The rectangular cross-sectional area of a metal brace is to have an area of 1875 square millimeters. The length is to be two and one-half times the width. Calculate the length to the nearest millimeter. Answer 1: 1339.3 mm Answer 2: 68.5 mm Answer 3: 535.7 mm Answer 4: 27.4 mm Correct Answer: 68.5 mm

Question 6: Two triangular pieces are cut from the rectangular aluminum sheet shown. After cutting the triangular pieces, what remains of the sheet will be discarded. Find the number of square feet of aluminum wasted. Round the answer to one decimal place. Answer 1: 6.8 sq ft Answer 2: 10.3 sq ft Answer 3: 1.5 sq ft Answer 4: 8.9 sq ft Correct Answer: 10.3 sq ft

Question 7: Determine the area of the template shown. Round the answer to the nearest square millimeter. Answer 1: 101 sq mm Answer 2: 2552 sq mm Answer 3: 1271 sq mm Answer 4: 4967 sq mm Correct Answer: 2552 sq mm

Question 8: A rectangular steel plate that is 22.30 inches long and 11.35 inches wide weighs 26.4 pounds. Find the weight of the sheet after five holes, each with a diameter of 5.25 inches, are cut. Round the answer to the nearest tenth of a pound. Answer 1: 15.1 pounds Answer 2: 13.9 pounds Answer 3: 17.6 pounds Answer 4: 19.2 pounds Correct Answer: 15.1 pounds

Question 9: Hydraulic pressure of 555.0 of pounds per square inch is exerted on a piston with a diameter of 2.950 inches. Find the total force, to the nearest pound, that is exerted on the piston. Answer 1: 5144 pounds Answer 2: 2572 pounds Answer 3: 3793 pounds Answer 4: 15,174 pounds Correct Answer: 3793 pounds

Question 10: Calculate the cross-sectional area, in square inches, of the machined part shown. Round the answer to the nearest tenth. Answer 1: 22.0 sq in Answer 2: 31.4 sq in Answer 3: 102.0 sq in Answer 4: 11.5 sq in Correct Answer: 31.4 sq in

GAMMA+ by Fox Valley Technical College is licensed under a Creative Commons Attribution 3.0 Unported License.

This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including, but not limited to, accuracy of information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership. Auxiliary aids and services are available upon request to individuals with disabilities. This equal opportunity program is part of a grant from the U.S. Department of Labor equaling $2,999,750.00.