Robotic Arc Welding Safety: Part 2 of 4 (WDRB13) The learner will identify safe practices for working with and around robotic arc welding equipment. Author - David Crawford

Question 1: What type of safety barrier is shown in the picture? Answer 1: E-Stop Answer 2: Light Curtain Answer 3: Pressure-Sensitive Floor Mat Answer 4: Interlock Device Correct Answer: Light Curtain

Question 2: What type of safety barrier is shown in the picture? Answer 1: E-Stop Answer 2: Interlock Device Answer 3: Pressure-Sensitive Floor Mat Answer 4: Light Curtains Correct Answer: Pressure-Sensitive Floor Mat

Question 3: What type of safety barrier is shown in the picture? Answer 1: E-Stop Answer 2: Pressure-Sensitive Floor Mat Answer 3: Light Curtains Answer 4: Interlock Device Correct Answer: Interlock Device

Question 4: When the robot is in normal operation, it is safe to assume what the robot's actions will be. Answer 1: True Answer 2: False Correct Answer: False

Question 5: Pinch points only exist when the robot is in normal operation. Answer 1: True Answer 2: False Correct Answer: False Feedback: Pinch points can exist any time an individual can get caught or injured by the motion of the robot or the cell's peripheral, including while programming.

Question 6: It is often necessary to enter a robot cell. What safety step must be considered before entering a cell? Answer 1: Always make sure another programmer is in control of the teach pendant. Answer 2: Do not enter unless the light curtain is enabled. Answer 3: Never enter a cell or the robot's envelope unless the robot has been disabled from automatic mode. Correct Answer: Never enter a cell or the robot's envelope unless the robot has been disabled from automatic mode.

Question 7: Before operating a robot cell, it is necessary for operators to be familiar with the location of all safety stops on the cell. Answer 1: True Answer 2: False Correct Answer: True

Question 8: Robotic welding cells often use shaded welding curtains. These curtains typically are not dark enough to allow an individual to watch the robot while welding. Answer 1: True Answer 2: False Correct Answer: True

Question 9: A robot that collides with a person will always stop before injury occurs. Answer 1: True Answer 2: False Correct Answer: False Feedback: Robots are industrial machines; their speed and power will easily overcome any human ability. The result will be serious injury or death.

Question 10: What type of safety device is shown in the picture? Answer 1: Collision Detect Answer 2: Dead Man's Switch Answer 3: Brake Release Correct Answer: Collision Detect

Question 11: What type of safety device is shown in the picture? Answer 1: Collision Detect Answer 2: Limit Switch Answer 3: Shock Sensor Answer 4: Dead Man's Switch Correct Answer: Collision Detect

Question 12: This type of safety device is typically used to limit the distance that a robot or other component of a robot cell can travel. Answer 1: Shock Sensor Answer 2: Dead Man's Switch Answer 3: Brake Answer 4: Limit Switch Correct Answer: Limit Switch

Question 13: Robots use a system of brakes to stop the arm and to hold it in position. What device is used to disengage the brakes and allow movement if necessary? Answer 1: Limit Switch Answer 2: Emergency Stop Answer 3: Brake Release Answer 4: Soft Stop (Hold Key) Correct Answer: Brake Release

Question 14: What type of safety device is shown in the picture? Answer 1: Emergency Stop Answer 2: Limit Switch Answer 3: Brake Release Answer 4: Pressure-Sensitive Floor Mat Correct Answer: Brake Release

Question 15: What type of safety device is shown in the picture? Answer 1: Dead Man's Switch Answer 2: Limit Switch Answer 3: Collision Detect Answer 4: Brake Release Correct Answer: Dead Man's Switch

GAMMA+ by Fox Valley Technical College is licensed under a Creative Commons Attribution 3.0 Unported License.

This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including, but not limited to, accuracy of information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership. Auxiliary aids and services are available upon request to individuals with disabilities. This equal opportunity program is part of a grant from the U.S. Department of Labor equaling $2,999,750.00.