Programming Basics: Part 1 of 2 (WDRB15) The learner will distinguish different concepts of robotic programming. Author - David Crawford

Question 1: What does TCP stand for? Answer 1: Torch Center Point Answer 2: Tool Center Point Answer 3: Tool Center Position Answer 4: Torch Center Position Correct Answer: Tool Center Point

Question 2: The mathematical point that a robot is moving through space: Answer 1: TCP Answer 2: Electrode Extension Answer 3: Endeffector Answer 4: Point-to-Point Correct Answer: TCP

Question 3: This form of motion control often uses mechanical stops or limit switches for each designated point. The design is often simple and used in repetitive tasks that do not require complicated motion. Answer 1: Controlled-Path Motion Answer 2: Continuous-Path Motion Answer 3: Point-to-Point Motion Answer 4: Pick-and-Place Motion Correct Answer: Pick-and-Place Motion

Question 4: This form of motion control involves teaching the robot a number of points in space. The positions are recorded and then played back. The result is a motion that travels the straight lines between points with no real control of the end effector between points. Answer 1: Point-to-Point Motion Answer 2: Pick-and-Place Motion Answer 3: Continuous-Path Motion Answer 4: Controlled-Path Motion Correct Answer: Point-to-Point Motion

Question 5: This is an extension of point-to-point motion. The difference is that this motion type can generate thousands of points much closer together, creating a smooth and continuous path. Answer 1: Point-to-Point Motion Answer 2: Controlled-Path Motion Answer 3: Continuous-Path Motion Answer 4: Pick-and-Place Motion Correct Answer: Continuous-Path Motion

Question 6: This is the most sophisticated method of motion control. The robot is programmed to move in a precisely controlled path from one point to the next. A linear movement and a circular movement are examples of this type of motion control. Speed and velocity are also precisely controlled for each movement of the robot or from one point to the next. Answer 1: Pick-and-Place Motion Answer 2: Continuous-Path Motion Answer 3: Point-to-Point Motion Answer 4: Controlled-Path Motion Correct Answer: Controlled-Path Motion

Question 7: Simple systems such as pick-and-place and point-to-point robots can be programmed this way. This programming method is more like machine set-up. An operator will set up the positions and make adjustments to any end stops, switches, or cams in the system. Answer 1: Manual Programming Answer 2: Teach Pendant Programming Answer 3: Walk-Through Programming Answer 4: Off-Line Programming Correct Answer: Manual Programming

Question 8: This method of programming uses a device that allows the operator to lead the robot through the positions and record points to memory. Answer 1: Teach Pendant Programming Answer 2: Manual Programming Answer 3: Off-Line Programming Correct Answer: Teach Pendant Programming

Question 9: This method of programming involves manually walking the robot through the steps and recording points. Thousands of points can be recorded, making a very smooth motion. Answer 1: Manual Programming Answer 2: Walk-Through Programming Answer 3: Off-Line Programming Correct Answer: Walk-Through Programming

Question 10: This type of programming has an advantage over on-line programming because the programmer does not have to take the robot out of production to create programs. This also allows a programmer to more easily write complex programs and spend less time programming. Answer 1: Manual Programming Answer 2: Teach Pendant Programming Answer 3: Walk-Through Programming Answer 4: Off-Line Programming Correct Answer: Off-Line Programming

Question 11: If a welding torch gets bent or damaged, the TCP will not line up with the weld wire. Answer 1: True Answer 2: False Correct Answer: True

Question 12: When a robot is shipped from the factory, it already knows where the end of the welding wire is in relationship to the end of the robot. Answer 1: True Answer 2: False Correct Answer: False Feedback: When a robot is shipped from the factory, it does not know what tool is being used. Therefore, a TCP must be defined by the user.

Question 13: A misaligned TCP is a common source of problems for welding quality and consistency. Answer 1: True Answer 2: False Correct Answer: True

Question 14: One TCP may be used for different tools on a robot. Answer 1: True Answer 2: False Correct Answer: False Feedback: Different tools have different center points, requiring a new TCP for each tool.

Question 15: A robot may have more than one TCP. Answer 1: True Answer 2: False Correct Answer: True Feedback: Some robots use multiple tools, and these may be changed out automatically. With each new tool, a new TCP must be used.

GAMMA+ by Fox Valley Technical College is licensed under a Creative Commons Attribution 3.0 Unported License.

This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including, but not limited to, accuracy of information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership. Auxiliary aids and services are available upon request to individuals with disabilities. This equal opportunity program is part of a grant from the U.S. Department of Labor equaling $2,999,750.00.