Cylinder Safety Review (WDST4) The learner will review safety precautions for the storage, handling, and use of cylinders. Author - Jessica Lloyd

Question 1: This is a safe way to handle a cylinder. Answer 1: True Answer 2: False Correct Answer: False Feedback: While it's safe to keep a cylinder on a welding cart, the cylinder must be secured to prevent it from falling.

Question 2: This device is used to: Answer 1: Indicate that the cylinder is empty Answer 2: Protect the cylinder valve from impact Answer 3: Cover the regulator gauges Correct Answer: Protect the cylinder valve from impact

Question 3: A cylinder should always be stored: Answer 1: In the upright position Answer 2: Stacked on its side Answer 3: With the cap on Answer 4: In the upright position and with the cap on Correct Answer: In the upright position and with the cap on

Question 4: What potential hazard is caused by tipping over an uncapped cylinder? Answer 1: It may become part of the electrical circuit Answer 2: The valve may break off Answer 3: The cylinder could explode Answer 4: Dirt may get in the valve Correct Answer: The valve may break off Feedback: While it's possible for a cylinder to rupture and explode due to circumstances such as electrical arc strikes and intense heat, it's more likely for the valve to break off when a cylinder tips over. In this case, the real hazard is that the cylinder will rapidly expel highly pressurized gas and shoot around like a rocket.

Question 5: What is this person doing? Answer 1: Opening the cylinder to begin welding Answer 2: Checking the cylinder's pressure Answer 3: "Cracking" the cylinder valve Answer 4: Attaching a regulator Correct Answer: "Cracking" the cylinder valve Feedback: Cracking the cylinder valve blows out dust and debris that could become lodged in the regulator. This is a good practice to follow every time you use a new cylinder.

Question 6: What are the possible consequences of leaving your cylinder valve open when its not in use? Answer 1: If it's leaking, you will continue to lose gas Answer 2: The regulator could become damaged Answer 3: The cylinder may tip over Answer 4: You could lose gas and the regulator could be damaged Answer 5: You could lose gas and the cylinder may tip over Correct Answer: You could lose gas and the regulator could be damaged

Question 7: What's the purpose of the soapy water test? Answer 1: To secure the cylinder Answer 2: To clean out dirt from the valve Answer 3: To make sure the regular isn't damaged Answer 4: To check for leaks Correct Answer: To check for leaks Feedback: Soapy water is used because of its tendency to bubble up when gas is leaking.

Question 8: Which of the following precautions should be taken when using a cylinder? Answer 1: Keep the cylinder chained up Answer 2: Avoid striking an arc against the cylinder Answer 3: Chain up the cylinder and avoid striking an arc against the cylinder Answer 4: Use oil to make sure there aren't any leaks Correct Answer: Chain up the cylinder and avoid striking an arc against the cylinder

Question 9: The most dangerous place to stand when opening a cylinder is: Answer 1: To the side of the regulator gauges Answer 2: Behind the regulator gauges Answer 3: In front of the regulator gauges Correct Answer: In front of the regulator gauges

Question 10: Damage to a regulator or flow meter occurs due to: Answer 1: Dropping or other impacts Answer 2: Being left pressurized when not in use Answer 3: Being used with normal working pressure Answer 4: Dropping or other impacts and being used with normal working pressure Answer 5: Dropping or other impacts and being left pressurized when not in use Correct Answer: Dropping or other impacts and being left pressurized when not in use

GAMMA+ by Fox Valley Technical College is licensed under a Creative Commons Attribution 3.0 Unported License.

This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including, but not limited to, accuracy of information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership. Auxiliary aids and services are available upon request to individuals with disabilities. This equal opportunity program is part of a grant from the U.S. Department of Labor equaling $2,999,750.00.