Lathe Cutting Speed and RPM Calculations (MTBS5214) In this learning activity the student will define cutting speed and calculate the proper revolutions per minute for turning applications. Author - Kelly Curran

Question 1: Cutting speed is the surface speed ______. Answer 1: where the cutting takes place Answer 2: of the spindle Answer 3: at the outside edge of the part Answer 4: at the center of the cutter Correct Answer: where the cutting takes place

Question 2: If two pieces of different diameters are operating at the same RPM, the larger diameter piece______. Answer 1: has a greater surface speed Answer 2: has a slower surface speed Answer 3: has the same surface speed as the smaller cutter Answer 4: None of the above Correct Answer: has a greater surface speed

Question 3: The harder the workpiece material, ______. Answer 1: the faster the cutting speed Answer 2: the slower the cutting speed Answer 3: the faster the RPM setting Answer 4: None of the above Correct Answer: the slower the cutting speed

Question 4: Calculate the RPM for turning a 0.500-inch diameter piece of 4140 steel with a cutting speed of 60 SFPM using a high-speed steel turning tool. Answer 1: 240 RPM Answer 2: 480 RPM Answer 3: 620 RPM Answer 4: 580 RPM Correct Answer: 480 RPM

Question 5: Calculate the RPM for turning a 2.500-inch diameter bar of 1045 steel with a carbide turning tool. The cutting speed for carbide turning tools in 1045 steel is 500 SFPM. Answer 1: 800 RPM Answer 2: 2400 RPM Answer 3: 3200 RPM Answer 4: 1600 RPM Correct Answer: 800 RPM

Question 6: Calculate the RPM for drilling a hole in a 6.0-inch diameter piece on a lathe with a 0.75-inch high-speed steel drill in 1095 steel. The cutting speed for 1095 steel is 40 SFPM. Answer 1: 240 RPM Answer 2: 480 RPM Answer 3: 215 RPM Answer 4: 315 RPM Correct Answer: 215 RPM

Question 7: Calculate the RPM for turning a 1.00-inch diameter piece of 52100 steel. The cutting speed for a high-speed steel turning tool in 52100 steel is 50 SFPM. Answer 1: 120 RPM Answer 2: 480 RPM Answer 3: 620 RPM Answer 4: 200 RPM Correct Answer: 200 RPM

Question 8: Calculate the RPM for boring a 0.7500 hole in a 3-inch diameter piece of 4140 steel. The cutting speed for a carbide-boring tool in 4140 steel is 240 SFPM. Answer 1: 320 RPM Answer 2: 1280 RPM Answer 3: 620 RPM Answer 4: 1580 RPM Correct Answer: 1280 RPM

Question 9: Calculate the RPM for turning a 4-inch piece of 1018 steel with a high-speed steel turning tool. The cutting speed for a high-speed steel tool in 1018 steel is 90 SFPM. Answer 1: 90 RPM Answer 2: 120 RPM Answer 3: 180 RPM Answer 4: 380 RPM Correct Answer: 90 RPM

Question 10: Calculate the RPM for rough turning a 4.00-inch diameter 1018 steel bar with a 55-degree carbide turning tool in 1018 steel. The cutting speed for a carbide turning tool in 1018 steel is 400 SFPM. Answer 1: 1000 RPM Answer 2: 800 RPM Answer 3: 600 RPM Answer 4: 400 RPM Correct Answer: 400 RPM

GAMMA+ by Fox Valley Technical College is licensed under a Creative Commons Attribution 3.0 Unported License.

This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including, but not limited to, accuracy of information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership. Auxiliary aids and services are available upon request to individuals with disabilities. This equal opportunity program is part of a grant from the U.S. Department of Labor equaling $2,999,750.00.