Carbide and Other Cutting Tool Materials - Set 1 (MTBS7914) The learner will identify cutting tool materials and compare the machinability of materials. Author - Kelly Curran

Question 1: Tungsten carbide (cemented carbide) is considered to be a composite material. Answer 1: True Answer 2: False Correct Answer: True

Question 2: Hard carbide and cobalt were sintered together to produce man-made: Answer 1: Platinum Answer 2: Diamonds Answer 3: Cubic zirconia Answer 4: Gold Correct Answer: Diamonds

Question 3: Other binder materials were tested and used to help with the resistance of: Answer 1: Stress cracks Answer 2: Built-up edges Answer 3: Cratering Answer 4: Excessive chip formation Correct Answer: Cratering

Question 4: Machinability factors are only limited to the type of material being machined. Answer 1: True Answer 2: False Correct Answer: False

Question 5: A material that is considered to be 100% machinable is: Answer 1: B1112 Answer 2: 1018 C.R.S. Answer 3: 12L14 Answer 4: 4140 P.H. Correct Answer: B1112

Question 6: Higher alloying contents in steels equates to better machinability. Answer 1: True Answer 2: False Correct Answer: False

Question 7: Tool life is affected by which of the following? Answer 1: Machine power/rigidity Answer 2: Part setup rigidity Answer 3: Tooling setup rigidity Answer 4: All of the above Correct Answer: All of the above

Question 8: Which tooling setup is the second-most accurate and rigid method of tool holding? Answer 1: Clamping an end mill in a spring collet holder Answer 2: Clamping an end mill in a solid holder with the set screw on the shank diameter of the tool Answer 3: Clamping an end mill in a solid holder with the set screw clamped to the set screw flat on the tool shank Answer 4: Clamping an end mill in a hydraulic or shrink fit holder Correct Answer: Clamping an end mill in a solid holder with the set screw clamped to the set screw flat on the tool shank

Question 9: Which tooling setup option is the least accurate, or rigid, method of tool holding? Answer 1: Clamping an end mill in a spring collet holder Answer 2: Clamping an end mill in a solid holder with the set screw on the shank diameter of the tool Answer 3: Clamping an end mill in a solid holder with the set screw clamped to the set screw flat on the tool shank Answer 4: Clamping an end mill in a hydraulic or a shrink fit holder Correct Answer: Clamping an end mill in a spring collet holder

Question 10: Work holding plays an important role in machinability factors. Answer 1: True Answer 2: False Correct Answer: True

Question 11: The average tool edge life expectancy of a coated carbide insert is approximately_______ in the cut. Answer 1: 30 to 40 minutes Answer 2: 5 to 10 minutes Answer 3: 18 to 20 minutes Answer 4: 60 minutes Correct Answer: 18 to 20 minutes

GAMMA+ by Fox Valley Technical College is licensed under a Creative Commons Attribution 3.0 Unported License.

This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including, but not limited to, accuracy of information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership. Auxiliary aids and services are available upon request to individuals with disabilities. This equal opportunity program is part of a grant from the U.S. Department of Labor equaling $2,999,750.00.