Drive Systems, Sensors & End Effectors: Part 1 of 2 (WDRB33) The learner will identify robotic drive systems, sensors, and end effectors. Author - David Crawford

Question 1: Commonly called a "Harmonic Drive," this type of drive system is more correctly known as: Answer 1: Strain Wave Gear Principle Answer 2: Wave Generation Theory Answer 3: Flexible Gear Drive Answer 4: Splined Gear Generator Correct Answer: Strain Wave Gear Principle

Question 2: If a robot is used to move very heavy parts, what type of power source should be used? Answer 1: Electric Answer 2: Steam Answer 3: Hydraulic Answer 4: Pneumatic Correct Answer: Hydraulic

Question 3: What type of motor is used in electric-powered robots for high precision and accuracy? Answer 1: Rectifier Resistor Answer 2: Diode Answer 3: Amplifier Coil Answer 4: Servo Correct Answer: Servo

Question 4: Gear systems are used in robots to achieve proper ratios. Which of the following gear systems is not used in precision robotics? Answer 1: The Cycloidal Gear System Answer 2: The Harmonic Drive Answer 3: The Planetary Gear System Correct Answer: The Planetary Gear System

Question 5: A welding torch, painting nozzle, and gripper are all considered to be _____ when attached to the end of a robot. Answer 1: A Transducer Answer 2: An End Effector Answer 3: A Drive System Answer 4: An Encoder Correct Answer: An End Effector

Question 6: What component is identified by letter A? Answer 1: Flexspline Answer 2: Circular Spline Answer 3: Wave Generator Correct Answer: Circular Spline

Question 7: What component is identified by letter B? Answer 1: Wave Generator Answer 2: Flexspline Answer 3: Circular Spline Correct Answer: Flexspline

Question 8: What component is identified by letter C? Answer 1: Wave Generator Answer 2: Flexspline Answer 3: Circular Spline Correct Answer: Wave Generator

Question 9: This rotational measuring device is rugged and is a type of electrical transformer. Answer 1: Resolver Answer 2: Encoder Correct Answer: Resolver

Question 10: This rotational measuring device is less rugged in demanding environments and uses a fixed number of increments on a rotating disk. Answer 1: Resolver Answer 2: Encoder Correct Answer: Encoder

GAMMA+ by Fox Valley Technical College is licensed under a Creative Commons Attribution 3.0 Unported License.

This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including, but not limited to, accuracy of information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership. Auxiliary aids and services are available upon request to individuals with disabilities. This equal opportunity program is part of a grant from the U.S. Department of Labor equaling $2,999,750.00.