GMAW: Equipment (WDEQ21) The learner will demonstrate knowledge of GMAW equipment. Author - David Crawford

Question 1: Which drive roll is used for GMAW of welding with steel electrode wires? Answer 1: V-Groove rolls Answer 2: U-Groove rolls Answer 3: Knurled rolls Correct Answer: V-Groove rolls

Question 2: Increased arc on time makes the puddle _________ and results in a flatter and smoother weld bead. Answer 1: denser Answer 2: higher and convex Answer 3: more fluid Correct Answer: more fluid

Question 3: If you could adjust the slope (as you can on some machines), what effect would a too steep slope have? Answer 1: The pinch effect will be applied rapidly and the molten drop will be violently "squeezed" off the electrode and cause excessive spatter. Answer 2: The short circuit current will rise rapidly to a high level. The pinch effect will also be high and the molten drop will separate violently from the wire. The excessive pinch effect will abruptly squeeze the metal aside, clear the short circuit, and create excessive spatter. Answer 3: The electrode will carry the full current, but the pinch effect may be too low to separate the drop and re-establish the arc. Under these conditions, the electrode will either pile up on the workpiece or freeze to the puddle. Correct Answer: The short circuit current will rise rapidly to a high level. The pinch effect will also be high and the molten drop will separate violently from the wire. The excessive pinch effect will abruptly squeeze the metal aside, clear the short circuit, and create excessive spatter.

Question 4: A power source without inductance has what effect? Answer 1: The short circuit current will rise rapidly to a high level. The pinch effect will also be high, and the molten drop will separate violently from the wire. The excessive pinch effect will abruptly squeeze the metal aside, clear the short circuit, and create excessive spatter. Answer 2: The electrode will carry the full current, but the pinch effect may be too low to separate the drop and re-establish the arc. Under these conditions, the electrode will either pile up on the workpiece or freeze to the puddle. Answer 3: The pinch effect will be applied rapidly and the molten drop will be violently "squeezed" off the electrode and cause excessive spatter. Correct Answer: The pinch effect will be applied rapidly and the molten drop will be violently "squeezed" off the electrode and cause excessive spatter.

Question 5: Increased arc on time makes the puddle more fluid and results in a _________ weld bead. Answer 1: flatter and smoother Answer 2: dense Answer 3: higher and convex Correct Answer: flatter and smoother

Question 6: In spray transfer, the addition of some inductance to the power supply will produce a __________ without affecting the steady-state welding condition. Answer 1: globular arc Answer 2: harder arc Answer 3: softer arc Answer 4: short circuit Correct Answer: softer arc

Question 7: If you could adjust the slope (as you can on some machines), what effect does little or no slope have? Answer 1: The short circuit current will rise rapidly to a high level. The pinch effect will also be high, and the molten drop will separate violently from the wire. The excessive pinch effect will abruptly squeeze the metal aside, clear the short circuit, and create excessive spatter. Answer 2: The pinch effect will be applied rapidly and the molten drop will be violently "squeezed" off the electrode and cause excessive spatter. Answer 3: The electrode will carry the full current, but the pinch effect may be too low to separate the drop and re-establish the arc. Under these conditions, the electrode will either pile up on the workpiece or freeze to the puddle. Correct Answer: The electrode will carry the full current, but the pinch effect may be too low to separate the drop and re-establish the arc. Under these conditions, the electrode will either pile up on the workpiece or freeze to the puddle.

GAMMA+ by Fox Valley Technical College is licensed under a Creative Commons Attribution 3.0 Unported License.

This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including, but not limited to, accuracy of information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership. Auxiliary aids and services are available upon request to individuals with disabilities. This equal opportunity program is part of a grant from the U.S. Department of Labor equaling $2,999,750.00.