Carbide and Other Cutting Tool Materials - Set 2 (MTBS108) The learner will identify cutting tool materials and compare the machinability of materials. Author - Kelly Curran

Question 1: Carbide inserts are made by a process called powder metallurgy. Answer 1: True Answer 2: False Correct Answer: True

Question 2: After the pressing stage of the powder metallurgy process, the product is in a _______ state and can be broken apart easily. Answer 1: Brown Answer 2: Green Answer 3: Red Answer 4: Blue Correct Answer: Green

Question 3: To ensure accuracy from one insert to the next, each insert undergoes a/an _________ process. Answer 1: Filing Answer 2: End milling Answer 3: Turning Answer 4: Grinding Correct Answer: Grinding

Question 4: Coatings are added to carbide cutting tools to improve wear resistance and ________ resistance. Answer 1: Appearance Answer 2: Rigidity Answer 3: Built-up edge Answer 4: Price Correct Answer: Built-up edge

Question 5: Carbide that has been coated using the PVD process has a smoother, brighter, and finer grain structure, resulting in a smoother cutting action. Answer 1: True Answer 2: False Correct Answer: True

Question 6: Carbide that has been coated using the CVD process is generally tougher but is prone to thermal cracking due to the higher temperature coating process. Answer 1: True Answer 2: False Correct Answer: True

Question 7: ___________ combines the benefits of different coatings and coating processes. Answer 1: Multi-layering Answer 2: Powder coating Answer 3: Powder heat treating Answer 4: All of the above Correct Answer: Multi-layering

Question 8: Coatings can also be used on other tooling and materials to improve wear resistance. Answer 1: True Answer 2: False Correct Answer: True

Question 9: Which tooling setup results in a more rigid and accurate method of tool holding? Answer 1: Clamping an end mill in a spring collet holder Answer 2: Clamping an end mill in a solid holder with the set screw on the shank diameter of the tool Answer 3: Clamping an end mill in a solid holder with the set screw clamped to the set screw flat on the tool shank Answer 4: Clamping an end mill in a hydraulic or a shrink fit holder Correct Answer: Clamping an end mill in a hydraulic or a shrink fit holder

Question 10: After the sintering or heat-treating process, the carbide has lost up to ____ of its size. Answer 1: 25 percent Answer 2: 75 percent Answer 3: 50 percent Answer 4: 90 percent Correct Answer: 50 percent

GAMMA+ by Fox Valley Technical College is licensed under a Creative Commons Attribution 3.0 Unported License.

This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including, but not limited to, accuracy of information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership. Auxiliary aids and services are available upon request to individuals with disabilities. This equal opportunity program is part of a grant from the U.S. Department of Labor equaling $2,999,750.00.