FCAW: Safety & Setup Set 1 (WDEQ12) The learner will demonstrate knowledge of flux-cored arc welding safety and setup. Author - David Crawford

Question 1: What should be on a cylinder valve that does not have a regulator attached? Answer 1: Flowmeter Answer 2: Cylinder cap Answer 3: Nothing - valve should be free and clear Answer 4: Regulator Correct Answer: Cylinder cap

Question 2: The first step to take when changing a shielding gas cylinder is: Answer 1: Turn gas off if left unattended for an extended period Answer 2: "Crack" the valve before attaching a regulator Answer 3: Turn the adjusting screw until proper pressure is obtained Answer 4: Properly secure the cylinder Correct Answer: Properly secure the cylinder

Question 3: The term "cracking" the valve means: Answer 1: Accidentally hitting the valve stem Answer 2: Accidentally hitting the valve stem and damaging it Answer 3: Slowly turning the valve on to blow out any obstruction in the valve Answer 4: Turning the valve off securely Correct Answer: Slowly turning the valve on to blow out any obstruction in the valve

Question 4: What does MSDS stands for? Answer 1: Material Safety Data Sheets Answer 2: Manufacturers Safety Data Sheets Answer 3: Material Safety Dated Sheets Answer 4: Material Safety Data Slips Correct Answer: Material Safety Data Sheets

Question 5: A shielding gas that is an asphyxiant means that it: Answer 1: Will not blanket the weld zone sufficiently Answer 2: Is highly volatile Answer 3: Is considered an explosive Answer 4: Will displace oxygen, making it difficult to breath Correct Answer: Will displace oxygen, making it difficult to breath

Question 6: Standing in water or in any moisture on the floor while welding can cause electrical shock. Answer 1: True Answer 2: False Correct Answer: True

Question 7: Welding with shielding gases high in argon will generate substantial ultraviolet radiation, which will react with oxygen in the vicinity of the arc to form ______________. Answer 1: Carbon monoxide Answer 2: Ozone Answer 3: Carbon dioxide Answer 4: Phosgene gas Correct Answer: Ozone

Question 8: Welding of stainless steel and surfaces with chromium alloys presents the problem of _______________ fumes. Answer 1: Carbon monoxide Answer 2: Hexavalent chromium Answer 3: Phosgene gas Answer 4: Carbide precipitated Correct Answer: Hexavalent chromium

Question 9: The heat and ultraviolet radiation from the arc causes the vapors from chlorinated hyrocarbons to decompose and form ______. Answer 1: Carbon monoxide Answer 2: Ozone Answer 3: Carbon dioxide Answer 4: Phosgene gas Correct Answer: Phosgene gas

Question 10: What is the suggested filter glass (comfort) for FCAW? Answer 1: Shade 5 to Shade 8 Answer 2: Shade 9 to Shade 11 Answer 3: Shade 11 to Shade 14 Answer 4: Shade 15 to Shade 20 Correct Answer: Shade 11 to Shade 14

GAMMA+ by Fox Valley Technical College is licensed under a Creative Commons Attribution 3.0 Unported License.

This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including, but not limited to, accuracy of information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership. Auxiliary aids and services are available upon request to individuals with disabilities. This equal opportunity program is part of a grant from the U.S. Department of Labor equaling $2,999,750.00.