Material Classification: Part 2 of 2 (WDTM25) The learner will identify different methods of material classifications. Author - David Crawford

Question 1: What is the minimum amount of carbon required to be considered a cast iron? Answer 1: 1.5% Answer 2: 2.0% Answer 3: 4.0% Answer 4: 6.0% Correct Answer: 2.0%

Question 2: Which of the following best describes cast irons? Answer 1: Not as brittle as steels. Answer 2: Have high compressive strengths. Answer 3: Have high tensile strengths. Correct Answer: Have high compressive strengths.

Question 3: Nodular/ductile cast iron has properties closest to those of steel. Answer 1: True Answer 2: False Correct Answer: True

Question 4: What does the first digit in the Aluminum Association system represent? Answer 1: Alloy type Answer 2: Percent carbon Answer 3: Aluminum purity Answer 4: Modifications to alloy Correct Answer: Alloy type

Question 5: Which materials have high thermal and electrical conductivity when compared to the others? Answer 1: Chromium and Nickel Answer 2: Iron and Copper Answer 3: Aluminum and Copper Answer 4: Nickel and Aluminum Correct Answer: Aluminum and Copper

Question 6: What material is similar to Aluminum? Answer 1: Magnesium Answer 2: Manganese Answer 3: Iron Answer 4: Tin Correct Answer: Manganese

Question 7: Which material has a high resistance to abrasion? Answer 1: Manganese Answer 2: Magnesium Answer 3: Iron Answer 4: Aluminum Correct Answer: Manganese

Question 8: Is a 1040 steel an alloy or a plain carbon steel? Answer 1: Alloy Answer 2: Plain Carbon Correct Answer: Alloy

Question 9: What is the carbon content of a 1040 steel? Answer 1: 4.0% Answer 2: 40% Answer 3: 0.4% Answer 4: .10% Correct Answer: 0.4%

Question 10: Is a 4130 steel an alloy or a plain carbon steel? Answer 1: Alloy Answer 2: Plain Carbon Correct Answer: Alloy

Question 11: What is the carbon content of a 4130 steel? Answer 1: 3.0% Answer 2: .30% Answer 3: 30% Answer 4: .41% Correct Answer: .30%

Question 12: Is an E52120 steel an alloy or a plain carbon steel? Answer 1: Alloy Answer 2: Plain Carbon Correct Answer: Alloy

Question 13: What is the carbon content of an E52120 steel? Answer 1: .20% Answer 2: 1.20% Answer 3: 12.0% Answer 4: .52% Correct Answer: 1.20%

GAMMA+ by Fox Valley Technical College is licensed under a Creative Commons Attribution 3.0 Unported License.

This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including, but not limited to, accuracy of information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership. Auxiliary aids and services are available upon request to individuals with disabilities. This equal opportunity program is part of a grant from the U.S. Department of Labor equaling $2,999,750.00.